PROGRAM 7
#Libraries
import RPi.GPIO as GPIO
import time

#GPIO Mode (BOARD / BCM)
GPIO.setmode(GPIO.BCM)

#set GPIO Pins
GPIO_TRIGGER = 18
GPIO_ECHO = 24

#set GPIO direction (IN / OUT)
GPIO.setup(GPIO_TRIGGER, GPIO.OUT)
GPIO.setup(GPIO_ECHO, GPIO.IN)

def distance():
    # set Trigger to HIGH
    GPIO.output(GPIO_TRIGGER, True)

    # set Trigger after 0.01ms to LOW
    time.sleep(0.00001)
    GPIO.output(GPIO_TRIGGER, False)

    StartTime = time.time()
    StopTime = time.time()

    # save StartTime
    while GPIO.input(GPIO_ECHO) == 0:
        StartTime = time.time()

    # save time of arrival
    while GPIO.input(GPIO_ECHO) == 1:
        StopTime = time.time()

    # time difference between start and arrival
    TimeElapsed = StopTime - StartTime
    # multiply with the sonic speed (34300 cm/s)
    # and divide by 2, because there and back
    distance = (TimeElapsed * 34300) / 2

    return distance

if __name__ == '__main__':
    try:
        while True:
        dist = distance()
        print ("Measured Distance = %.1f cm" % dist)
        time.sleep(1)

        # Reset by pressing CTRL + C
    except KeyboardInterrupt:
        print("Measurement stopped by User")
        GPIO.cleanup()

OUTPUT:
Measured Distance = 3341.0 cm
Measured Distance = 18.2 cm
Measured Distance = 18.1 cm
Measured Distance = 18.2 cm
Measured Distance = 13.5 cm
Measured Distance = 11.7 cm
Measured Distance = 9.9 cm
Measured Distance = 7.6 cm
Measured Distance = 229.5 cm
Measured Distance = 228.4 cm
Measured Distance = 0.8 cm
Measured Distance = 11.9 cm
Measured Distance = 11.2 cm
Measured Distance = 10.4 cm
Measured Distance = 10.8 cm